#### 2.5.5.1 ACWR(AC-97 Mixer Read/Write Register)

Address		:  AudioBase + 40h

Size		:  32 bits

Type		:  Read /Write

# Default		:  00000000h

# Write

Bit 7..0		X	index of the AC-97 mixer register to be written;

Bit 7=0	for Primary CODEC;

Bit 7=1	for Secondary CODEC(Reserved).

Bit 8		0	Read Mixer Register

1	Write Mixer Register

Bit 11.9		X	reserved

Bit 12		Select bit of Modem-write-AC97 request.

0	Modem request AC97 write by setting reg40 bit[13];

1	Modem request AC97 write by assert signal ‘mdm_cmd_rqst’ internally.

Bit 14..13	00	clear request to write AC97 mixer register

01	S/W Modem driver request to write AC97 mixer register

10	S/W Audio driver request to write AC97 mixer register

11	forbidden

Bit 15

0	force to clear Reg40h_B15 and Reg44h_B15 hardware busy flag

1	write AC-97 mixer register (indexed by bit 7..0) with bit 31..16;

Bit 31..16	X	data to be written into AC-97 mixer register;

# Read

Bit 7..0		X	index of the AC-97 mixer register to be written;

Bit 7=0	for Primary CODEC;

Bit 7=1	for Secondary CODEC(Reserved).

Bit 8		0	Bit 31 – 16 is register value of last read cycle

1	Bit 31 – 16 is register value to write Codec97

Bit 11.9		X	reserved

Bit 12		Select bit of Modem-write-AC97 request.

0	Modem request AC97 read/write by setting reg40 bit[13];

1	Modem request AC97 read/write by assert signal ‘mdm_cmd_rqst’ internally.

Bit 13		0	S/W Modem driver is not granted to read/write AC97 mixer register

1	S/W Modem driver is granted to read/write AC97 mixer register

Bit 14		0	S/W Audio driver is not granted to read/write AC97 mixer register

1	S/W Audio driver is granted to read/write AC97 mixer register

Bit 15		0	ready to read/write AC-97 mixer register

1	busy reading/writing AC-97 mixer (indexed by Bit 7..0);

Bit 31..16	X	data to be read from/written into AC-97 mixer register.